## Slide 1: Introduction to Slurm & Slurm Batch Scripts
Ashley Dederich
Research Consulting & Faculty Engagement
Center for High Performance Computing
ashley.dederich@utah.edu

## Slide 2: Overview of Talk
What is Slurm, and why use it?
Preparing a Job with Slurm
  Two (Main) Methods: Batch and Interactive
Batch Mode
  Slurm Batch Directives
  Accounts and Partitions
  CHPC Storage Resources
Basic Slurm Commands
Interactive Mode
Using GPU Nodes
Job Priority & Performance
Notes: 1/27/26

## Slide 3: Overview of Talk
What is Slurm, and why use it?
Preparing a Job with Slurm
  Two (Main) Methods: Batch and Interactive
Batch Mode
  Slurm Batch Directives
  Accounts and Partitions
  CHPC Storage Resources
Basic Slurm Commands
Interactive Mode
Using GPU Nodes
Job Priority & Performance
Notes: 1/27/26

## Slide 4: Re-cap of Resources
CHPC resources:
  HPC clusters:
    General Environment: Granite, Notchpeak, Kingspeak, Lonepeak
    Protected Environment (PE): Redwood
    Others
  VM (Windows, Linux)
  Storage
  Other Services
Condominium mode:
  HPC Cluster = CHPC-owned nodes (general nodes) + PI-owned nodes (owner nodes)
  All CHPC users have access to CHPC-owned resources for free. Some clusters (notchpeak) need allocations (peer-reviewed proposals)
  Owners (PI group) have the highest priority using owner nodes
  All CHPC users have access to owner nodes in Guest mode for free (jobs subject to preemption)

## Slide 5: What is Slurm?
Formerly known as Simple Linux Utility for Resource Management
Open-source workload manager for supercomputers/clusters
  Manage resources (nodes/cores/memory/interconnect/gpus)
  Schedule jobs (queueing/prioritization)
Used by 60% of the TOP500 supercomputers1
Fun fact: development team based in Lehi, UT
[1] https://en.wikipedia.org/wiki/Slurm_Workload_Manager (2023 Jun)

## Slide 6: What is Slurm …and why use it?
Goal: you, the user, want to connect to the CHPC machines and analyze some data using R
So, you connect to one of our clusters
You don’t want to analyze your data on the login node…

## Slide 7: What is Slurm …and why use it?
The login node has limited resources
You could guess that, in this example, just a few people could overload the login node
Nobody could login, edit files, etc…

## Slide 8: What is Slurm …and why use it?
*Slurm allows users to request a compute job to run on compute nodes
Notes: So, how do we go about asking SLURM to submit a job for us?

## Slide 9: What is Slurm …and why use it?
So, how do we ask Slurm to submit a job?
We need to ask for the correct resources
But first, we need to know what those resources are…

## Slide 10: Overview of Talk
What is Slurm, and why use it?
Preparing a Job with Slurm
  Two (Main) Methods: Batch and Interactive
Batch Mode
  Slurm Batch Directives
  Accounts and Partitions
  CHPC Storage Resources
Basic Slurm Commands
Interactive Mode
Using GPU Nodes
Job Priority & Performance
Notes: 1/27/26

## Slide 11: Two Main Slurm Modes
Batch Mode
  Non-Interactive (hands-off)
  Great for complete workflows

## Slide 12: Two Main Slurm Modes
Batch Mode
  Non-Interactive (hands-off)
  Great for complete workflows
Interactive Mode
  Complete work on a compute node interactively
  Great for debugging, immediate feedback of commands

## Slide 13: Overview of Talk
What is Slurm, and why use it?
Preparing a Job with Slurm
  Two (Main) Methods: Batch and Interactive
Batch Mode
  Slurm Batch Directives
  Accounts and Partitions
  CHPC Storage Resources
Basic Slurm Commands
Interactive Mode
Using GPU Nodes
Job Priority & Performance
Notes: 1/29/26

## Slide 14: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the temporary directory
SCRDIR=/scratch/general/vast/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#copy over input files
cp file.input $SCRDIR/
cd $SCRDIR
#Set up whatever package we need to run with
module load <some-module>
#Run the program with our input
myprogram < file.input > file.output
#Move files out of working directory and clean up
cp file.output $HOME/.
cd $HOME
rm -rf $SCRDIR
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the scratch directory
set SCRDIR /scratch/local/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#move input files into scratch directory
cp file.input $SCRDIR/
cd $SCRDIR
#Set up whatever package we need to run with
module load <some-module>
#Run the program with our input
myprogram < file.input > file.output
#Move files out of working directory and clean up
cp file.output $HOME/.
cd $HOME
rm -rf $SCRDIR
Notes: This is what a slurm script looks like all together. It looks like a lot of information at first, but lets break it down piece by piece.

## Slide 15
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
Notes: The first thing you will need to fill out are the #SBATCH directives. Lets focus on the most important part – account and partition

## Slide 16: Overview of Talk
What is Slurm, and why use it?
Preparing a Job with Slurm
  Two (Main) Methods: Batch and Interactive
Batch Mode
  Slurm Batch Directives
  Accounts and Partitions
  CHPC Storage Resources
Basic Slurm Commands
Interactive Mode
Using GPU Nodes
Job Priority & Performance
Notes: 1/29/26

## Slide 17: Preparing a Slurm Job
To run a job on CHPC, you need to specify a correct Partition, QOS, & Account combination.
  Commands to check valid pairs:
  mysinfo, mysqueue,
  mychpc batch (Method 3; gives info on all clusters)
Notes: NOTE: are the first two commands useful to show?
First two commands are limited to the cluster you currently reside on
Here is how you can use the myallocation command

## Slide 18: Preparing a Slurm Job
mychpc batch
Helpful command; shows what resources you have access to
Allocation state
qos
account
partition
Notes: Cluster, account, and partition are information you will need to submit a SLURM job.

## Slide 19: Allocation State
Four allocation states:
  General: you can run jobs on that cluster with no issues
  Owner: you own a node and have priority access to it (preempt guest jobs)
  Data Transfer: this partition is solely for use of transferring data – not for computational work
  Preemptable*: you can still run jobs, but they are subject to preemption.
*Preemption: your job will run on that node until another job requests that same node, at which point your job is automatically cancelled.
Notes: Preemption sounds scary but isn’t something you should worry about. We will get back to preemption later.

## Slide 20: Account
Account: to limit and track resource utilization at user/group level.
A user/group can have multiple Slurm accounts
  each represents different privileges.

## Slide 21: Partition
Refers to a set of nodes with specific resources:
<cluster> : CHPC-owned resources; node sharing by default
<cluster>-guest: lab-owned resources used in guest mode; node sharing by default; subject to preemption
<cluster>-gpu: use nodes with GPUs; node sharing by default
<pi>-<cl>: lab-owned resources used in owner mode; node sharing by default

## Slide 22
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --time=02:00:00 specifies wall time of a job in Hours:Minutes:Seconds
#SBATCH -t 02:00:00
also works

## Slide 23: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --nodes=1 specifies number of nodes
#SBATCH -N 1
also works

## Slide 24
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --ntasks=8 total number of CPUs per node
#SBATCH -n 8
also works

## Slide 25: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --mem=32GB specifies total memory per node
#SBATCH --mem=0 gives you memory of whole node

## Slide 26
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH -o outputs standard output in the form slurmjob-<JOBID>.out-<NODEID>
#SBATCH -e outputs error messages in the form slurmjob-<JOBID>.err-<NODEID>

## Slide 27: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --constraint <CONSTRAINTS>
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --constraint <CONSTRAINTS>
Can also include constraints to target specific nodes
This can be memory avail, cpu count, specific owner nodes, etc

## Slide 28
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --constraint “c40”
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --constraint “m768”
Can also include constraints to target specific nodes
This can be memory avail, cpu count, specific owner nodes, etc

## Slide 29: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --constraint “c40&m768”
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --constraint “c40|c36”
Can also include constraints to target specific nodes
This can be memory avail, cpu count, specific owner nodes, etc
Include c40 AND m768 nodes
Include c40 OR c36 nodes

## Slide 30
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --constraint “gompert”
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --constraint “gompert|schmidt|tbicc”
Can also include constraints to target specific nodes
This can be memory avail, cpu count, specific owner nodes, etc
https://www.chpc.utah.edu/usage/constraints/
Notes: But, for now, we don’t want to worry about constraints

## Slide 31: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --mail-type=FAIL,BEGIN,END
#SBATCH --mail-user=ashley.dederich@utah.edu
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#SBATCH --mail-type=FAIL,BEGIN,END
#SBATCH --mail-user=ashley.dederich@utah.edu
Can also have Slurm email you with updates
Useful to monitor the status of jobs without constantly checking via squeue
Notes: But, for now, we don’t want to worry about constraints
#SBATCH --mail-type=FAIL,BEGIN,END
#SBATCH --mail-user=ashley.dederich@usu.edu

## Slide 32
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the temporary directory
SCRDIR=/scratch/general/vast/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#copy over input files
cp file.input $SCRDIR/.
cd $SCRDIR
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the scratch directory
set SCRDIR /scratch/local/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#move input files into scratch directory
cp file.input $SCRDIR/.
cd $SCRDIR
Now, we will discuss the best way to stage your files for analysis
Notes: This is what a slurm script looks like all together. It looks like a lot of information at first, but lets break it down piece by piece.

## Slide 33: Overview of Talk
What is Slurm, and why use it?
Preparing a Job with Slurm
  Two (Main) Methods: Batch and Interactive
Batch Mode
  Slurm Batch Directives
  Accounts and Partitions
  CHPC Storage Resources
Basic Slurm Commands
Interactive Mode
Using GPU Nodes
Job Priority & Performance
Notes: 1/29/26

## Slide 34: CHPC Storage Resources
Home
Scratch
Group
Free
Automatically provisioned
50GB soft limit
Free
For intermediate files required during a job
vast – 50TB/user quota
nfs1 – no quota
Needs to be purchased by PI
By the TB
Notes: We have three main storage systems here
We recommend using scratch when running your job
Here is how you can go about doing that

## Slide 35: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the temporary directory
SCRDIR=/scratch/general/vast/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#copy over input files
cp file.input $SCRDIR/.
cd $SCRDIR
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the scratch directory
set SCRDIR /scratch/local/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#move input files into scratch directory
cp file.input $SCRDIR/.
cd $SCRDIR
Create an environmental variable that points to scratch path
Points to your uNID
Points to your uNID
Notes: Create environmental var
$USER
Notice $SLURM_JOB_ID – lets talk about this

## Slide 36: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the temporary directory
SCRDIR=/scratch/general/vast/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#copy over input files
cp file.input $SCRDIR/.
cd $SCRDIR
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the scratch directory
set SCRDIR /scratch/local/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#move input files into scratch directory
cp file.input $SCRDIR/.
cd $SCRDIR
Create the working directory
Notes: Create environmental var
$USER
Notice $SLURM_JOB_ID – lets talk about this

## Slide 37: Slurm Environment Variables
Some useful environment variables:
  $SLURM_JOB_ID
  $SLURM_SUBMIT_DIR
  $SLURM_NNODES
  $SLURM_NTASKS
Can get them for a given set of directives by using the env command inside a script (or in a srun session).
  See: https://slurm.schedmd.com/sbatch.html#SECTION_OUTPUT-ENVIRONMENT-VARIABLES
Notes: SLURM sets environmental variables for us that we can call in our script, including $SLURM_JOB_ID
There is a whole bunch of different vars that slurm sets, you can see a complete list at this link, available in the pdf of these slides.
Back to our regularly scheduled programming

## Slide 38: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the temporary directory
SCRDIR=/scratch/general/vast/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#copy over input files
cp file.input $SCRDIR/.
cd $SCRDIR
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the scratch directory
set SCRDIR /scratch/local/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#move input files into scratch directory
cp file.input $SCRDIR/.
cd $SCRDIR
Create the scratch directory
Notes: Create environmental var
$USER
Notice $SLURM_JOB_ID – lets talk about this

## Slide 39
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the temporary directory
SCRDIR=/scratch/general/vast/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#copy over input files
cp file.input $SCRDIR/.
cd $SCRDIR
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the scratch directory
set SCRDIR /scratch/local/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#move input files into scratch directory
cp file.input $SCRDIR/.
cd $SCRDIR
Copy over input files and move on over to $SCRDIR

## Slide 40: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the temporary directory
SCRDIR=/scratch/general/vast/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#copy over input files
cp file.input $SCRDIR/.
cd $SCRDIR
#Set up whatever package we need to run with
module load <some-module>
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the scratch directory
set SCRDIR /scratch/local/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#move input files into scratch directory
cp file.input $SCRDIR/.
cd $SCRDIR
#Set up whatever package we need to run with
module load <some-module>
Load the desired modules
Notes: Load the desired modules into your environment so that the computer can recognize the commands you are giving it

## Slide 41
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the temporary directory
SCRDIR=/scratch/general/vast/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#copy over input files
cp file.input $SCRDIR/.
cd $SCRDIR
#Set up whatever package we need to run with
module load <some-module>
#Run the program with our input
myprogram < file.input > file.output
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the scratch directory
set SCRDIR /scratch/local/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#move input files into scratch directory
cp file.input $SCRDIR/.
cd $SCRDIR
#Set up whatever package we need to run with
module load <some-module>
#Run the program with our input
myprogram < file.input > file.output
Run the program you need to
Notes: This is what a slurm script looks like all together. It looks like a lot of information at first, but lets break it down piece by piece.

## Slide 42: Slurm File Structure (in sh and tcsh)
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the temporary directory
SCRDIR=/scratch/general/vast/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#copy over input files
cp file.input $SCRDIR/.
cd $SCRDIR
#Set up whatever package we need to run with
module load <some-module>
#Run the program with our input
myprogram < file.input > file.output
#Move files out of working directory and clean up
cp file.output $HOME/.
cd $HOME
rm -rf $SCRDIR
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the scratch directory
set SCRDIR /scratch/local/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#move input files into scratch directory
cp file.input $SCRDIR/.
cd $SCRDIR
#Set up whatever package we need to run with
module load <some-module>
#Run the program with our input
myprogram < file.input > file.output
#Move files out of working directory and clean up
cp file.output $HOME/.
cd $HOME
rm -rf $SCRDIR
Copy output to your $HOME
Move back to $HOME
Move back to $HOME
Remove $SCRDIR
Remove $SCRDIR
Copy output to your $HOME
Notes: Finally, you clean up after yourself.
Removing $SCRDIR is the most important part, because the scratch directories (vast and nfs1) frequently fill up and we have to remind users to clean up those directories.

## Slide 43: Example Slurm Script – sh, tcsh
#!/bin/bash
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the temporary directory
SCRDIR=/scratch/general/vast/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#copy over input files
cp file.input $SCRDIR/.
cd $SCRDIR
#Set up whatever package we need to run with
module load <some-module>
#Run the program with our input
myprogram < file.input > file.output
#Move files out of working directory and clean up
cp file.output $HOME/.
cd $HOME
rm -rf $SCRDIR
#!/bin/tcsh
#SBATCH --account=owner-guest
#SBATCH --partition=kingspeak-guest
#SBATCH --qos=kingspeak-guest
#SBATCH --time=02:00:00
#SBATCH --nodes=1
#SBATCH --ntasks=8
#SBATCH --mem=32G
#SBATCH -o slurmjob-%j.out-%N
#SBATCH -e slurmjob-%j.err-%N
#set up the scratch directory
set SCRDIR /scratch/local/$USER/$SLURM_JOB_ID
mkdir -p $SCRDIR
#move input files into scratch directory
cp file.input $SCRDIR/.
cd $SCRDIR
#Set up whatever package we need to run with
module load <some-module>
#Run the program with our input
myprogram < file.input > file.output
#Move files out of working directory and clean up
cp file.output $HOME/.
cd $HOME
rm -rf $SCRDIR
Done! Let’s call this file
FirstSlurmScript.sbatch
Notes: And there you have it! You have a whole SLURM script.

## Slide 44: Overview of Talk
What is Slurm, and why use it?
Preparing a Job with Slurm
  Two (Main) Methods: Batch and Interactive
Batch Mode
  Slurm Batch Directives
  Accounts and Partitions
  CHPC Storage Resources
Basic Slurm Commands
Interactive Mode
Using GPU Nodes
Job Priority & Performance
Notes: 1/27/26

## Slide 45: Basic Slurm commands
sbatch FirstSlurmScript.sbatch - launch a batch job
Job ID
Notes: sbatch is the command to use. If your #SBATCH directives have no errors, you will see a message pop up that looks like this…
This is the SLURM job id

## Slide 46: Basic Slurm commands
sbatch FirstSlurmScript.sbatch - launch a batch job
squeue - shows all jobs in queue
  squeue --me - shows only your jobs
  squeue -u <uNID> - shows only your jobs
  mysqueue* - shows job queue per partition and associated accounts you have access to on the cluster
*CHPC developed programs. See CHPC Newsletter 2023 Summer
Notes: Give demonstration

## Slide 47: Basic Slurm commands
sbatch FirstSlurmScript.sbatch - launch a batch job
squeue - shows all jobs in queue
  squeue --me - shows only your jobs
  squeue -u <uNID> - shows only your jobs
  mysqueue* - shows job queue per partition and associated accounts you have access to on the cluster
scancel <jobid> - cancel a job
*CHPC developed programs. See CHPC Newsletter 2023 Summer
scancel 13335248

## Slide 48: Basic Slurm commands
sbatch FirstSlurmScript.sbatch - launch a batch job
squeue - shows all jobs in queue
  squeue --me - shows only your jobs
  squeue -u <uNID> - shows only your jobs
  mysqueue* - shows job queue per partition and associated accounts you have access to on the cluster
scancel <jobid> - cancel a job
sinfo - shows all partitions/nodes state
  mysinfo* - info on partitions/nodes and associated accounts you have access to on the cluster
*CHPC developed programs. See CHPC Newsletter 2023 Summer
Notes: Give example of sinfo –help, sinfo –p notchpeak-guest, sinfo -N

## Slide 49: Basic Slurm commands
sbatch FirstSlurmScript.sbatch - launch a batch job
squeue - shows all jobs in queue
  squeue --me - shows only your jobs
  squeue -u <uNID> - shows only your jobs
  mysqueue* - shows job queue per partition and associated accounts you have access to on the cluster
scancel <jobid> - cancel a job
sinfo - shows all partitions/nodes state
  mysinfo* - info on partitions/nodes and associated accounts you have access to on the cluster
salloc – start an interactive job
  Works with same #SBATCH directives
*CHPC developed programs. See CHPC Newsletter 2023 Summer
Notes: The last thing you can do is request an interactive node through SLURM with the salloc command
Useful if you have a program that you need to interact with through the command line
Works with same #SBATCH directives
Give a demonstration salloc –partition notchpeak-shared-short –account notchpeak-shared-short –N 1 –t 01:00:00

## Slide 50: Basic Slurm commands
sbatch FirstSlurmScript.sbatch - launch a batch job
squeue - shows all jobs in queue
  squeue --me - shows only your jobs
  squeue -u <uNID> - shows only your jobs
  mysqueue* - shows job queue per partition and associated accounts you have access to on the cluster
scancel <jobid> - cancel a job
sinfo - shows all partitions/nodes state
  mysinfo* - info on partitions/nodes and associated accounts you have access to on the cluster
salloc – start an interactive job
  Works with same #SBATCH directives
*CHPC developed programs. See CHPC Newsletter 2023 Summer
**note** – all of these commands only work on the cluster you are currently logged into.
To recognize a different cluster, use these flags:
-M all
-M kingspeak
--clusters all
--clusters kingspeak
Notes: The last thing you can do is request an interactive node through SLURM with the salloc command
Useful if you have a program that you need to interact with through the command line
Works with same #SBATCH directives
Give a demonstration salloc –partition notchpeak-shared-short –account notchpeak-shared-short –N 1 –t 01:00:00

## Slide 51: Overview of Talk
What is Slurm, and why use it?
Preparing a Job with Slurm
  Two (Main) Methods: Batch and Interactive
Batch Mode
  Slurm Batch Directives
  Accounts and Partitions
  CHPC Storage Resources
Basic Slurm Commands
Interactive Mode
Using GPU Nodes
Job Priority & Performance
Notes: 1/29/26

## Slide 52: Interactive Mode
Why interactive?
  Useful for getting immediate feedback from commands
  Great for debugging

## Slide 53: Interactive Mode
Why interactive?
  Useful for getting immediate feedback from commands
  Great for debugging
An interactive command is launched through the salloc command

## Slide 54: Interactive Mode
Why interactive?
  Useful for getting immediate feedback from commands
  Great for debugging
An interactive command is launched through the salloc command salloc --time=8:00:00 -–ntasks=4 --nodes=1 –-mem=16G --account=<account> --partition=kingspeak

## Slide 55: Interactive Mode
Why interactive?
  Useful for getting immediate feedback from commands
  Great for debugging
An interactive command is launched through the salloc command salloc --time=8:00:00 -–ntasks=4 --nodes=1 –-mem=16G --account=<account> --partition=kingspeak
Use of FastX connection is highly recommended
  support GUI applications
  keep your sessions alive

## Slide 56: Interactive Mode
Why interactive?
  Useful for getting immediate feedback from commands
  Great for debugging
An interactive command is launched through the salloc command salloc --time=8:00:00 -–ntasks=4 --nodes=1 –-mem=16G --account=<account> --partition=kingspeak
Use of FastX connection is highly recommended
  support GUI applications
  keep your sessions alive
Open OnDemand is another option to start interactive sessions

## Slide 57: Interactive Mode
Beginning an interactive Slurm session:
Exiting from an interactive Slurm session:
started on notchpeak1
login node
Slurm job ID
Node assigned, automatic
ssh to compute node
Slurm job
cancelled
Brought back
to login node

## Slide 58: Overview of Talk
What is Slurm, and why use it?
Preparing a Job with Slurm
  Two (Main) Methods: Batch and Interactive
Batch Mode
  Slurm Batch Directives
  Accounts and Partitions
  CHPC Storage Resources
Basic Slurm Commands
Interactive Mode
Using GPU Nodes
Job Priority & Performance
Notes: 1/29/26

## Slide 59: Slurm for use of GPU Nodes
GPU nodes are on all clusters
Info on GPU nodes found at https://chpc.utah.edu/documentation/guides/gpus-accelerators.php
There are both general (open to all users) and owner GPU nodes (available via owner-gpu-guest, with preemption, to all uses)
At this time, most general GPU nodes are run without allocation (no charge)
  Granite GPUs run with allocation
  Must get added to the gpu accounts – Request via helpdesk@chpc.utah.edu
GPU partitions set up in a shared mode only as most codes do not yet make efficient use of multiple GPUs so we have enabled node sharing
Use only if you are making use of the GPU for the calculation

## Slide 60: Node Sharing on GPU nodes
In addition to selecting a GPU partition, you should:
#SBATCH --gres=gpu #at a minimum
#SBATCH --gres=gpu:<gpu-type>:<gpu-count>
Option | Explanation
#SBATCH --gres=gpu:p100:1 | request one p100 GPU
#SBATCH --mem=4G | request 4 GB of RAM (default is 2GB/core if not specified)
#SBATCH --mem=0 | request all memory of the node; use this if you do not want to share the node as this will give you all the memory
#SBATCH --ntasks=1 | request 1 cpu core

## Slide 61: GPU Job
#SBATCH --time 10:00:00
#SBATCH --partition=notchpeak-gpu
#SBATCH --account=notchpeak-gpu
#SBATCH --qos=notchpeak-gpu
#SBATCH --nodes=1
#SBATCH --ntasks=4
#SBATCH --mem=16G
#SBATCH --gres=gpu:a100:1
#SBATCH --mail-type=FAIL,BEGIN,END
#SBATCH --mail-user=name@example.com
#SBATCH -o slurm-%j.out-%N
#SBATCH -e slurm-%j.err-%N

## Slide 62: Overview of Talk
What is Slurm, and why use it?
Preparing a Job with Slurm
  Two (Main) Methods: Batch and Interactive
Batch Mode
  Slurm Batch Directives
  Accounts and Partitions
  CHPC Storage Resources
Basic Slurm Commands
Interactive Mode
Using GPU Nodes
Job Priority & Performance
Notes: 1/29/26

## Slide 63: Job Priority
Slurm assigns each job a priority score
Priority score = how fast your job will start

## Slide 64: Job Priority
Combination of four factors add to base priority (QOS)
  Time in queue (most important)
  Fairshare
  Job size
  # jobs in last 2 weeks
Only 5 jobs per user per slurm account (qos) will accrue priority
sprio gives job priority for all jobs
  sprio –j <JOBID> for a given job
  sprio –u <UNID> for user’s jobs
https://www.chpc.utah.edu/documentation/software/slurm.php#priority

## Slide 65: Checking Job Performance
Why check job performance?
If you use more resources than your job needs…
- It counts against your allocation
- Potential for longer wait times in cue
Notes: This is useful for checking if you need to update memory, cpu, or node counts for a job – if you are using too many resources, it counts against your allocation and potential for longer wait times in cue

## Slide 66: Checking Job Performance
With an active job
  Can ssh to node
    Useful commands: top, ps, sar, atop
  - Also from interactive node can query job with pestat
    pestat --help
  - Can query node status
    scontrol show node notch024
After job completes -- XDMoD Supremm
  Job level data available day after job ends
  XDMoD sites https://xdmod.chpc.utah.edu and https://pe-xdmod.chpc.utah.edu
  Usage info: https://www.chpc.utah.edu/documentation/software/xdmod.php
Notes: Multiple ways you can check job performance

## Slide 67: Useful Aliases
si/si2 – check node specifications (CPU, Memory, GPU, PI)
sq – check job priority, assigned nodes, reason/error…
Bash to add to .aliases file:
alias si="sinfo -o \"%20P %5D %14F %8z %10m %10d %11l %16f %N\""
alias si2="sinfo -o \"%20P %5D %6t %8z %10m %10d %11l %16f %N\""
alias sq="squeue -o \"%8i %12j %4t %10u %20q %20a %10g %20P %10Q %5D %11l %11L %R\""
Csh/Tcsh to add to .aliases file:
alias si 'sinfo -o "%20P %5D %14F %8z %10m %11l %16f %N"'
alias si2 'sinfo -o "%20P %5D %6t %8z %10m %10d %11l %N"'
alias sq 'squeue -o "%8i %12j %4t %10u %20q %20a %10g %20P %10Q %5D %11l %11L %R"‘
See: https://www.chpc.utah.edu/documentation/software/slurm.php#aliases

## Slide 68: Slurm Documentation at CHPC
https://www.chpc.utah.edu/documentation/software/slurm.php
https://www.chpc.utah.edu/documentation/software/serial-jobs.php
https://www.chpc.utah.edu/documentation/software/node-sharing.php
https://www.chpc.utah.edu/usage/constraints/
https://www.chpc.utah.edu/documentation/guides/index.php#GenSlurm
Other good documentation sources
http://slurm.schedmd.com/documentation.html
http://slurm.schedmd.com/pdfs/summary.pdf
http://www.schedmd.com/slurmdocs/rosetta.pdf

## Slide 69: Getting Help
CHPC website documentation
  www.chpc.utah.edu
    Getting started guide, cluster usage guides, software manual pages, CHPC policies
Email: helpdesk@chpc.utah.edu
Help Desk: 405 INSCC
We use chpc-hpc-users@lists.utah.edu for sending messages to users
Notes: Will be changing to web maintenance.